|  | ......................... pcs. .............................. € .............................. € GEZE Slimdrive SCR-FR RC2 Modular, compact automatic curved sliding door (360°) with a drive height of only 70 mm for use in escape and rescue routes, RC 2 tested in accordance with DIN EN 1627 through 1630, TÜV type-tested in accordance with DIN 18650/EN 16005, in 2-motor technology, fine-framed in light-coloured transparent design, unusually spacious, with a freely selectable diameter between 2700 mm and 3500 mm. Redundant emergency exit function through 2-motor technology, with duplicate processing system and low-maintenance Monitored rechargeable battery for emergency opening in the event of a power failure Latest software for optional Bluetooth connection to a PC for convenient parameter setting, commissioning and after-sales service maintenance Redundant digital control performance level "d" according to DIN EN ISO 13849): - Self-learning - Optimum convenience thanks to automatic adaptation of door behaviour to traffic - Can be networked and integrated in building systems via CAN-bus - Independent fault detection and protocol - Adjustment options for all door movement parameters - All functions integrated in one unit, no further modules necessary - Stainless steel floor guide fully embedded in the floor - Reinforced roller carriage guide - Additional mechanical securing features in ceiling area Two extremely quiet running direct current drives, for leaf weights up to 120 kg Robust power supply with integrated all-pole main switch and fuse protection Static and dynamic power limitation in accordance with DIN 18650/EN 16005 Automatic reversal when obstacles are detected Additional variants for more safety and convenience: ( ) FR-RWS For use in emergency exit systems with locked escape route and emergency opening switch, with TÜV report for enabling in individual cases (has to be applied for by the client) * ( ) FR-LL For locked one-way or shop closed function, TÜV type-tested ( ) FR-DUO With emergency exit function in both directions, TÜV type-tested *The use of an emergency push button is compulsory for the RWS operating mode, with all other variants an emergency command device (emergency stop switch) does not have to be used. Construction dimensions (dimensions in unfinished state): Outside diameter: .............mm, freely selectable between 2700 and 3500 mm, Clear passage height PH: .............mm freely selectable up to 3000 mm Total height of door system: .............mm Passage clearance PC: ............mm Note: Other dimensions on request! Moving leaf of exterior door: Moving leaf with VSG safety glass fine-framed (up to 120 kg leaf weight): ( ) with VSG glass (based on P4A) 11 mm Side parts of exterior door: side parts with VSG safety glass, fine-framed ( ) with VSG glass (based on P4A) 11 mm Moving leaf of interior door: ( ) Fine-framed with GEZE profile system VSG 10 mm, clear Side parts of interior door: ( ) Curved VSG 10 mm, clear or ( ) Curved thermally insulated panel lining, 22 mm thick or ( ) Smooth-surface thermally insulated panels, approx. 34 mm thick Frame doorway RC2: Aluminium framework construction in the same colour as the system for installation of the doors in a façade tested to RC 2 or in a wall construction built in accordance with the requirements of EN 1627. Max. width 300 mm ( ) Implementation as sandwich profile ( ) Implementation as box profile Aluminium ceiling construction: ( ) Standard height 70 mm or ( ) Raised ceiling canopy .............mm, with perimeter canopy cover made of curved aluminium sheets Roof covering outside: ( ) Metal cover plate or ( ) Waterproof roof with 2 water spouts (flat roof without gradient) Roof covering inside: ( ) Metal cover plate or ( ) Glass roof with metal cover over the drive unit Locking: - Bi-stable electromechanical rod locking, invisibly integrated in the profile system, with manual emergency unlocking in the drive Surface of the light alloy parts: ( ) Powder coating RAL colours or ( ) LM anodised E6/EV1 or ( ) Colour anodised ............ Floor ring ( ) GEZE 360° stainless steel (V2A) floor ring is used as floor covering edging at the same time. ( ) Sheet metal base 100 mm and/or ( ) Swivel flange (30 x 5 mm) and/or ( ) Floor plate with discharge nozzle Note: The insulation of the building is a contracted service and must be carried out on site. Floor cover ( ) GEZE floor mat, anthracite colour, 22 mm, more colours available on request! or ( ) 18 mm coconut matting in natural colours (delivery only, laying by the technical crew of the floor fitters) or ( ) 4 mm black rubber nap mat (delivery only, laying by the technical crew of the floor fitters) or ( ) Floor cover to be carried out on site Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, acceptance testing, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650/EN 16005 through plant fitters or service partner. In compliance with DIN 18650/EN 16005: - Safety analysis must be carried out as a basis for planning and execution - A regular inspection must be carried out at least 1 x year and after-sales service maintenance at least 2 x year NOTE: The burglar-resistant function RC 2 is only enabled in "NIGHT" mode of operation. In the "NIGHT" mode of operation the door does not fulfil any escape route requirements. It is necessary to ensure that there is nobody in the building or that sufficient other emergency exits are available. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Operation GEZE display programme switch in the AS 500 range for setting the mode of operation as well as for commissioning and parameterisation of the drive, with function keys, 2x 7-segment display, alphanumerical fault display, IP rating IP 40 Operating modes: permanently open, automatic, shop closing, night-locking, off ( ) Surface-mounted ( ) Flush-mounted or GEZE key programme switch for setting the operating mode, with control keys, LED dot display, coded error display, IP rating IP 40, suitable for switch product ranges with 55 x 55 mm switch insert Operating modes: off, permanently open, automatic, shop closing-time, night-locking ( ) Surface-mounted ( ) Flush-mounted or GEZE mechanical programme switch* for setting the operating mode, with key, LED fault display, IP rating IP 40, suitable for switch programmes with 55 x 55 mm switch insert Operating modes: off, permanently open, automatic, shop closing-time, night-locking ( ) Surface-mounted ( ) Flush-mounted * According to AutSchR and DIN 18650/EN 16005 the programme switch must be secured against unauthorised adjustment on FR doors: GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the operating mode, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 363+ combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling ( ) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Activation and protection (optional position) GC 365 combined detector with direction detecting radar movement detector for activation and active infrared detector with two light curtains for protection of the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) outside ( ) inside Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the sensor in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 339+ active infrared detector with two light curtains for protecting the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling ( ) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 341 active infrared detector with two light curtains for protecting the opening or closing area according to DIN 18650/EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE elbow switch, plastic, IP rating IP 30 Dimensions: 90 x 180 x 23 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) Surface-mounted ( ) Rear panel for attaching the elbow switch to glass (in connection with the transmitting module) or GEZE elbow switch, LS990, IP rating IP 30 Dimensions: 81 x 223 x 51 mm ( ) white ( ) stainless steel ( ) optional transmitting module ( ) Surface-mounted ( ) Flush-mounted or GEZE elbow switch, stainless steel, IP rating IP 65 Dimensions: 72 x 250 x 17 mm ( ) Surface-mounted or GEZE non-contact proximity switch (radar) Plastic with antimicrobial surface, IP rating IP65, multi-colour LED feedback, adjustable acoustic feedback. Additional input to actively change the LED colour. Dimensions: 80 x 80 mm ( ) Flush mounting 12 mm deep ( ) Surface mounting 21 mm deep ( ) Variant for WC or GEZE LED sensor push button, plastic, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor push button, glass, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor foot switch, glass, IP rating IP69K Dimensions: 100 x 100 x 3 mm ( ) flush-mounting ( ) vertically adjustable installation base for depths of up to 215 mm from the unfinished floor |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE wireless programme with secure rolling code encryption for wireless activation of the drive (approx. 30 m range in the building). Transmitter: ( ) Wireless transmitter with 1 key, IP rating IP 54 and wall fixing ( ) Wireless transmitter with 2 keys, IP rating IP 54 and wall fixing ( ) Wireless transmitter with 4 keys, IP rating IP 54 and wall fixing ( ) Transmitting module for optional integration in GEZE elbow switches Receiver: ( ) Receiving module with 2 outputs, 24 V, pulse mode or pulse and permanent mode for installation in the drive or in a flush-mounted box with IP rating IP 20 |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE GCER 300, 1-door SET Access control solution with RFID reader and PIN keypad in stand-alone operation for controlling one door (can be extended to 2 doors). RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Two authorisation types for short-time release or continuous release (office function). Configurable door release time. Variable PIN length. Communication between reader and control unit takes place by encrypted data transfer. Functions such as interlocking door system or dementia adjustable. Release buttons can be connected. Set comprising: 1 pc. GEZE GCER 300 I/O Box (ID no. 185707) 1 pc. GEZE GCVR 300 T, RFID reader flush-mounted (ID no. 185708) 2 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE GCVR Touch 300 T, RFID reader flush-mounted (ID no. 187108) GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (Id. no. 130024) or GEZE GCER 300 Light, 1-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation with a relay output for controlling one door located in the secured inner area. RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised for short-time release. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Configurable door release time. Variable PIN length. Communication takes place via encrypted data transfer. Set comprising: 1 pc. GEZE GCER 300 Light, RFID reader flush-mounted (ID no. 185710) 1 pc. GEZE GCER 300 system card master (ID no. 185713) 10 pc. GEZE RFID ID card (ID no. 185711) Optional GEZE RFID key fob (ID no. 185712) GEZE GCER AP surface-mounted frame (ID no. 130024) Accessories for GCER 300 / GCER 300 Light Plug-in power supply NT 1.0 A – 24 V DC (optional) Primary: 230 V AC, 50 Hz Secondary: 24 V DC (+/- 5 %) / 1 A (ID no. 130025) Power supply NT 1.1 A – 24 V DC flush-mounted (optional) For installation in deep standard flush-mounted boxes Primary: 230 V AC, 50 Hz Secondary: 24 V DC / 1.1 A (ID no. 151426) Power supply NT 1.5 A – 24 V DC HA (optional) For installation on top hat rails Primary: 230 V AC, 50 Hz Secondary: 21.6 – 26.4 V DC / 1.5 A (ID no. 151425) |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54) with or without profile half cylinder and switch function ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54) with or without profile half cylinder and hold-open function for the fire service ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE key switch outside (IP rating IP 54), prepared for on site profile half cylinder of closing system and 1 push button switch with key symbol for opening from the inside. On contact, the system opens from its locked position once outwards and inwards, and locks again after the leaf has reached the closed position. |
|  | ......................... pcs. .............................. € .............................. € Safeguarding (optional position) GEZE emergency stop switch with glass pane and lighting for switching off the mains voltage, IP rating IP 20 An emergency command device (emergency stop switch) is not essential in accordance with DIN 18650/EN 16005. ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Safeguarding (optional position) GEZE emergency stop switch with illuminated mushroom button for emergency opening or emergency unlocking, IP rating IP 40 An emergency command device (emergency stop switch) is not essential in accordance with DIN 18650/EN 16005. ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Lighting (optional position) ( ) ..... pcs. LED spotlight (max. 1 W per light) integrated in the soffit or ( ) ..... pcs. recess for lighting to be installed on site (diameter = ..... mm) |
|  | ......................... pcs. .............................. € .............................. € Locking (optional position) ( ) Electromagnetic locking, integrated in the drive unit, with manual emergency unlocking (standard only in the external door) and in addition ( ) Bolt lock for fine-framed door leaves for installation in the bottom door shoe profile, prepared for profile cylinder and/or profile half cylinder, lockable on one side (profile half cylinder 46 mm long) |
|  | ......................... pcs. .............................. € .............................. € Hot-air curtain system (optional position) ( ) Hot-air curtain system integrated in the suspended ceiling construction of the curved sliding door. ( ) Blow-out channel in the canopy area (minimum canopy height 350 mm) or ( ) Blow-out channel in the suspended soffit (canopy height 70 mm) Hot-air curtain system design with: ( ) Electric connection: Heat output: ............kW/ Amount of air.........m³/h ( ) Hot water connection Heat output: ............kW/ Amount of air.........m³/h Note: The power of the hot-air curtain equipment included in the offer has not been calculated by us; the dimensioning and specification of the hot-air curtains must be carried out by the specialist planner responsible. |
|  | ......................... pcs. .............................. € .............................. € Façade connection (optional position) Off-centre façade connection ( ) Connections and installation of the curved sliding door off-centre to the façade and/or ( ) Larger side parts which turn the arch into an oval system. Details and dimensions on request. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |