|  | ......................... pcs. .............................. € .............................. € Number codelock Toplock CTI, in metal casing, with black keypad, for entering 1 to 6-digit codes, 5 opening codes possible, potential-free relay output as closer contact Switching time approx. 2 seconds Switching load: max. 24 V DC / 1 A Operating voltage: 12 - 24 V DC, 12 V AC IP rating: IP 65 Dimensions (W x H x D): 80 x 80 x 15 mm (ID no. 090061) |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Number codelock Toplock CTI B, in metal casing, with illuminated black keypad, for entering 1 to 6-digit codes, 5 opening codes possible, potential-free relay output as closer contact Switching time approx. 2 seconds Switching load: max. 24 V DC / 1 A Operating voltage: 12 - 24 V DC, 12 V AC IP rating: IP 66 Dimensions (W x H x D): 60 x 126 x 22.5 mm (ID no. 090063) |
|  | ......................... pcs. .............................. € .............................. € Number codelock Toplock CTS V, in metal casing, with vandalism-proof metal keypad, incl. separate evaluation unit, for entering 1 to 6-digit codes, 5 opening codes possible, potential-free relay output as nightlatch function contact Switching time approx. 2 seconds Switching load: max. 250 V / 5 A Operating voltage: 230 V AC IP rating: IP 65 IP rating of the evaluation unit: IP 43 Dimensions (W x H x D): 80 x 80 x 15 mm (keypad) 110 x 188 x 40 mm (evaluation unit) (ID no. 090077) |
|  | ......................... pcs. .............................. € .............................. € Number codelock Toplock CTS BV, in metal casing, with illuminated vandalism-proof metal keypad, incl. separate evaluation unit, for entering 1 to 6-digit codes, 5 opening codes possible, potential-free relay output as nightlatch function contact Switching time approx. 2 seconds Switching load: max. 250 V / 5 A Operating voltage: 230 V AC IP rating: IP 65 IP rating of the evaluation unit: IP 43 Dimensions (W x H x D): 60 x 126 x 22.5 mm (keypad) 110 x 188 x 40 mm (evaluation unit) (ID no. 090079) Power supplies for CTI / CTI B |
|  | ......................... pcs. .............................. € .............................. € Power supply NET 320 For installation in flush-mounted socket Plastic housing, cast module Primary: Voltage supply 230 V AC, 50 Hz Secondary: Voltage supply 24 V DC (+/- 5 %) Current output 750 mA, 18 W Dimensions: 55.7 x 33 mm (dia.xD) |
|  | ......................... pcs. .............................. € .............................. € Power supply NT 12-1A For installation in flush-mounted socket or surface-mounted housing Primary: Voltage supply 230 V AC, 50 Hz Secondary: Voltage supply 12 V DC (+/- 5 %) Output current: 1 A Power: 12 W Operating temperature: -10 °C to +50 °C IP rating: IP 20 Dimensions (W x H x D): 50.8 x 54 x 32 mm (ID no. 160148) |
|  | ......................... pcs. .............................. € .............................. € Plug-in power supply NT 1.0 A – 24 V DC Direct-voltage power supply device Primary: Voltage supply 230 V AC, 50 Hz Secondary: Voltage supply 24 V DC Output current: 1 A (ID no. 130025) |